USB 3.0

USB 3.0 introduces a variety of new features that improve performance, reduce system power consumption, and extend functionality. The key features include:

1. Improved performance using new SuperSpeed data rates.
2. Improved protocols
  — End-to-End Protocol (Based on Token/Data/Handshake)
  – Data Bursting
  – Bulk Streaming
  — Port-to-Port Protocol (also called Link-to-Link Protocol)
3. Enabling of new host controllers that handle all device speeds and protocols while reducing overall link and system power consumption.

The SuperSpeed bus is maintaining backward compatibility to the existing Low-, Full- and High-Speed devices, and backward compatibility for SuperSpeed devices so they can operate at one or more of the USB 2.0 speeds.

USB 3.0 Host Controllers:-

In order to support all of the enhancements afforded by the USB 3.0 specification, a new generation of USB 3.0 host controllers is required. While other USB 3.0 host controller implementations are possible, many of the principal USB 3.0 host controllers released thus far are compatible with the eXtensible Host Controller Interface (xHCI) specification.

Key motivations for new controllers such as xHCI include:
Combining support for legacy USB 2.0 low speed (LS), full speed (FS), and high speed (HS) transactions with the new USB 3.0 SuperSpeed (SS) transactions — essential in handling high bandwidth bulk streaming transfers to large-capacity mass storage devices.
Improved power efficiency at both the bus/device and platform levels. This is becoming critical with the huge growth of mobile and embedded battery powered platforms.

There are few applications that require the SuperSpeed performance at this time. However, solid state drives and video and audio are some of the applications that can currently take advantage of the current SuperSpeed transfer rate of 5 Gigabits/second. In addition, the higher speed enables more demanding applications for the future.

USB Bandwidth Comparison:-

USB Speed	Bit Rate	Max Bytes/sec	Introduced
Low Speed	1.5Mb/sec	187.5KB/s	Jan, 1995
Full Speed	12Mb/sec	1.5 MB/sec	Jan, 1995
High Speed	480Mb/sec	60MB/sec	April, 2000
SuperSpeed	5Gb/sec	500MB/sec	Dec, 2008

There are a variety of host controllers, including:
1. UHCI (Universal Host Controller Interface) — handles only low- and fullspeed devices
2. OHCI (Open Host Controller Interface) — handles only low- and full-speed devices
3. EHCI (Enhanced Host Controller Interface) — handles high-speed devices directly and low- and full-speed devices that attach beneath high-speed hubs that implement a transaction translator.
The most common implementation is an EHCI controller combined with one or more UHCI or OHCI companion controllers.

The Port Routing logic is controlled by EHCI software that tests each port to determine whether a high-speed, full-speed or low-speed device is attached.
The EHCI retains all high-speed devices and connects full- and low-speed devices to the UHCI companion controllers.

The Protocols :-
The End-to-End protocols define a set of protocol layer packets used in transferring information between the host controller and device endpoints. The protocol varies depending on the type of endpoint being accessed and whether the data movement is IN or OUT.

The Protocol Packet Types
SuperSpeed USB uses a collection of header packets that originate at and are received by the Protocol layer. These Protocol layer packets are categorized as four primary types by the specification.

Protocol Packet Types and Characteristics:-
Name	Type Code	Sub-Types
Link Management Packets	00000b	6
Transaction Packets	00100b	8
Data Packet	01000b	NA
Isochronous Timestamp Packet	01100b	NA

The host controller initiates each transaction sequence by sending a token packet (e.g., ACK packet for IN tokens and DATA packet for OUT tokens). The SuperSpeed End-to-End protocol defines the sequence of packets exchanged between the host controller and targeted USB device. Three categories of protocol layer packets are used in conjunction with the End-to-End protocol:

-> Transaction Packets (TPs) — these packets are all Header packets and include seven SubTypes that in general emulate the token/data/handshake sequence, control data flow and manage End-to-End connectivity.
-> Data Packet — this packet is categorized separately from the Transaction Packet because it consists of both a Header packet and the Data Packet Payload (DPP). In some cases errors may result in the payload being dropped in which case the End-to-End protocol will detect the missing payload and retransmit the Data packet.
-> Isochronous Timestamp Packet (ITP) — this header packet is the only broadcast packet used in the SuperSpeed protocol and is a replacement for the Start of Frame (SOF) packet used by the USB 2.0 bus implementation.
As its name indicates the ITP carries bus timing information that is broadcast to all devices in the network that are ready to accept the packet.

USB 3.0 Hubs

SuperSpeed hubs contain two separate hub functions: one for SuperSpeed operations and one for the USB 2.0 (i.e., Low-, Full- and High-Speed) operations.

SuperSpeed hub functionality:-
-> Responding to Software Requests including:
— GetDescriptor (Device, Configuration, String, Hub, etc.)
— SetAddress
— SetConfiguration
— SetPortPower
 — GetPortStatus, etc.
-> Forwarding Packet in both directions.
-> Managing packet routing in the downstream direction.
-> Managing the link power hierarchy
-> Transaction Deferral
-> Hub Error Detection and Handling.