UVC

Video Interface Subclass and Protocol
The Video Interface class is divided into subclasses as identified by the Interface Subclass code.
The following two interface subclasses are defined in this specification.
 VideoControl Interface
 VideoStreaming Interface
The following Function Subclass is used in the Interface Association Descriptor.
 Video Interface Collection

Video Function Topology:-
To be able to manipulate the physical properties of a video function, its functionality must be
divided into addressable entities. The following two generic entities are identified:
=> Units
=> Terminals
Units provide the basic building blocks to fully describe most video functions. Video functions are built by connecting together several of these Units. A Unit has one or more Input Pins and a single Output Pin, where each Pin represents a cluster of logical data streams inside the video
function.

There are two types of Terminals. An Input Terminal (IT) is an entity that represents a starting point for data streams inside the video function. An Output Terminal (OT) represents an ending point for data streams. From the video function’s perspective, a USB endpoint is a typical example of an Input Terminal or Output Terminal. It either provides data streams to the video function (IT) or consumes data streams coming from the video function (OT). Likewise, a Charge Coupled Device (CCD) sensor, built into the video function is represented as an Input Terminal in the video function’s model. Connection to a Terminal is made through its single Input Pin or Output Pin.